## Slide 2: Standard TCP
It is a connection oriented protocol
It has been tuned to work for networks composed of wired links and stationary hosts
It is a reliable protocol;
The number of packet sent is regulated by increase or decrease size of the window
TCP sender uses the cumulative acknowledgements sent by the receiver.
To adapt with the problems of wired link the window size is changed

## Slide 3: Congestion
The network involved in wired data transmission like fiber optics copper wires etc works without introducing transmission errors
If a software is mature enough it will not drop packets or flip bits so a packet drop cannot be due to hardware or software error
So the reason for packet loss is some overload in transmission path i.e. congestion
Congestion is a condition when the buffers of the router are filled, the sum of input rates of packet is greater than output link. The router cannot forward the packets fast enough and drop the packets.

## Slide 4: Congestion control
Slow start
Congestion Avoidance
Fast Retransmit

## Slide 5: Slow start
Sender calculates congestion window for the receiver
The transmission starts with congestion window (cwnd=1)
Sender sends one packet; If acknowledgement received increase window size by 1 i.e. 2
Sender now sends two packets; If acknowledgement received for two packets, window is increased by 2 one for each acknowledgement i.e. 4
For each received acknowledge TCP increase the window exponentially only upto a threshold

## Slide 6: Congestion control
As soon as congestion threshold is received, window is increased linearly by adding 1 to the congestion window each time acknowledgement is received
it continues to increase its window size linearly until
  it reaches the receiver’s maximum advertised window or
  packet loss is observed due to time-out
  duplicate acknowledgement is received for same packet

## Slide 7: How packet loss is identified??
TCP measures how long acknowledgements take to return back and use it to determine which packets have reached the receiver .
For this purpose, it maintains a running average of round trip delay and an estimate of expected deviation from this average
If current delay is longer then average by more than 4 times expected deviation, TCP assumes packet loss and retransmits

## Slide 8: How packet loss is identified???
Duplicate acknowledgement: acknowledgement for same packet received again and again
This is because receiver acknowledges higher in order sequence number. If it receives out-of-order packets, it also generates acknowledgements for same highest in order sequence number
If it receives out-of-order sequence number and that result in duplicate acknowledgement. In this case also it assumes packet loss but not due to congestion due to error on the link
If it receives 3 duplicate acknowledgements then it activates fast retransmit algorithm.
It assumes data segment indicated by duplicate acknowledgements is lost and retransmits only lost segment. This is known as fast retransmission(RFC 2001 & RFC 2581)
No time is wasted waiting for timeout in order for

## Slide 9: Fast retransmission
Sequence#1→Sent : ACK for 1 received
Sequence#2→Sent : ACK for 2 received
Sequence#3→Sent : ACK not received
Sequence#4→Sent: received at receiver but ACK for 3 sent by receiver
Sequence#5→Sent: received at receiver but ACK for 3 sent by receiver
Sequence#6→Sent: received at receiver but ACK for 3 sent by receiver
Number of duplicate acknowledgement is 3 !!!
Packet 3 is lost!!!
Only sequence number 3 is retransmitted

## Slide 10: Actions performed when packet loss is identified
Dropping threshold value into half the current window or 2 whichever is larger
Resetting the transmitting window size to 1 activating slow start
Reset retransmission timer to a back off interval that doubles with each consecutive timeout

## Slide 11
Can standard TCP replicated in wireless environment as well???
NO
There are many other reasons for packet loss in wireless environment other than congestion

## Slide 12: Reasons of packet loss in wireless environment
High Bit Error rate: Wireless links suffers from a high bit error rate high BER causes packets to be corrupted resulting in loss of TCP data segments or acknowledgements FEC at data link may handle high BER but it would be wastage of wireless bandwidth when correction is not necessary
Black outs: When the mobile move from one cell to another call or service is transferred from old base station called Handoff. Hard Handover- there is brief disconnection known as black out period. Any packet sent during this period might be lost.
Call Blocking: Disconnections due to call blocking; a condition when mobile station do not get any channel due to unavailability of the channels.

## Slide 13: Reasons of packet loss in wireless environment
Disconnection due to small cell latencies: When the cell sizes are small to accommodate more and more users and increase the capacity results in small cell latencies and hence frequent disconnection.
Signal Blocking: When radio signals are blocked due to buildings and other objects in the environment
Power Scarcity: Mobile computer are battery operated hence power required is more

## Slide 14
Specialized algorithms are necessary optimized for wireless communications

## Slide 15: Goals of optimized algorithms
Not possible to change the entire TCP because it is the base on which the entire internet is based
The protocol should not go into slow start when it is not genuine to go
Isolate the mobility related problems from existing network protocols when fixed host and wireless station to communicate

## Slide 16: I-TCP
Mobile host
access point
(foreign agent)
wired Internet
Optimized TCP
standard TCP
Fixed host

## Slide 17
An End-to End TCP connection between fixed host and mobile host is split into 2 separate connections at MSR (Mobility support router)
MSR can be an access point, foreign agent incase mobile IP, entry point of network like IWF in GSM, GGSN in case of GPRS.
The link between fixed computer and AP is supported by regular TCP and between MSR and mobile node optimized TCP is used

## Slide 18: Packet sent from fixed host to mobile host
Sender sends packet to MSR
It acts as proxy; buffers the packets ; gives acknowledgement to the receiver
MSR then forwards packet to mobile host
If packet is lost on wired link, standard TCP handles it
If packet lost on wireless link, MSR retransmits with low round trip time

## Slide 19: Packet sent from fixed host to mobile host
Mobile host
Access point
(foreign agent)
Fixed host
Packet
ACK
Packet
ACK
Sender sends packet to MSR ;It acts as proxy; buffers the packets ; gives acknowledgement to the receiver
MSR then forwards packet to mobile host;If packet is lost on wired link, standard TCP handles it
If packet lost on wireless link, MSR retransmits with low round trip time

## Slide 20: Packet sent from mobile host to fixed host
Mobile node sends the packet
MSR acknowledges it and forwards to the fixed computer
If packet is lost, it is retransmitted on wireless with lower round trip time

## Slide 21: Handovers
At the time of handover old proxy forwards the packets to the new proxy because acknowledgements are already sent for those packets
New MSR then forwards those packets to the mobile host
Current state of TCP (sequence numbers, address, ports)reflected by socket should also be migrated

## Slide 22: Software components
MH Side:
  I-TCP can be accessed as a transport protocol by application running on mobile host using special library calls
  They are similar in interface and function to the socket calls made by an application using regular or standard end – to – end TCP
MSR Side:
  It consists of a user level UNIX process pumping data from one part of connection to the other
  Hand off support for I-TCP connection is implement in MSR kernels

## Slide 23: Advantages
  No need to make changes in TCP protocol used by computers in fixed network or any other device which do not need optimization
  Transmission error on wireless links do not propagate in fixed network
  The optimized TCP is used only on wireless link without affecting stability of internet

## Slide 24: Disadvantages
Loss of end-to-end semantics packets already acknowledgements before being delivered
Whole scheme fails if MSR crashes
Increased handover tendency
Foreign Agents should be a trusted entity. Security threat if MSR is compromised