## Slide 2: Communication entities: Data, Signals, Transmission and Channel
Data is the entity that is to be exchanged between different computers(voice, number, image..)
Signals electrical or electromagnetic representation of data
Data transmission is communication of data by the transmission or propagation of electromagnetic signals through either wired/wireless media (channel)

## Slide 3: Analog vs. Digital signal
Analog signal
  Continuous signal
  Uses continuous range of values to represent information
  denoted by sine waves
  Analog technology records waveforms as they are
  Sine waves
Digital signals
  discrete time signals
  denoted by square waves
  Uses discrete or discontinuous values to represent information
  Samples analog waveforms into a limited set of numbers and records them
  Square waves

## Slide 4: Analog vs. Digital Representation
Analog Signal
Digital Signal

## Slide 5: Electro magnetic waves
Electrons when propagated either in a guided media or free space follow a wave like pattern
They have both an electrical as well as a magnetic field associated with them
Hence the waves are electro magnetic waves
All of these waves vary with time in direction and intensity.
They move with speed of light in vaccum; Speed decreases after entering materials
They move through vacuum, and do not need a medium to travel

## Slide 6: Examples in day to day life
Light
Voice
Radio waves…..

## Slide 7: Representation of E.M. wave
Function of Time
Function of Frequency
TIME
AMPLITUDE
FREQUENCY
AMPLITUDE

## Slide 8: Attributes of an E.M. wave
Amplitude
Frequency
Wavelength
Phase

## Slide 9: Periodic vs. Aperiodic waves
TIME
AMPLITUDE
TIME
AMPLITUDE
Periodic wave: Repeats itself over time
(Sine wave )
Aperiodic wave: Does not repeats itself over time

## Slide 10: Mathematical representation
S(t)= A sin (2 Л f t + Ф)
A = Amplitude; f = Frequency; t = Period;Ф = Phase
TIME
AMPLITUDE
t
A

## Slide 11: Parameters : Amplitude
Amplitude: Maximum value or strength of the signal over time. Unit is volts
A = 1
A = 2
A = 3
A = -1
A = 0.5
A = -2

## Slide 12: Frequency
f = 3; t = 1/3 sec.
f = 1 ; t = 1 sec
f = 2 ; t = 1/2 sec
f = 0.5 ; t = 2sec
Frequency(ν): Number of cycles per unit time. Unit is hertz
Time period(T) : Amount of time taken to complete one cycle. Unit is sec, ms…etc.
T = 1/f

## Slide 13: Phase shift
Phase shift : 0
Phase shift : 90
Phase shift : -90
Phase shift : 180
Phase Shift
Shift from the origin Unit is degrees or radians
A negative phase shift indicates a movement to the right, and a positive phase shift indicates movement to the left.

## Slide 14: Wave length
Wave Length
Distance covered by one cycle. Distance between two peak values of a wave
Represented by symbol λ
Unit is unit of distance
As frequency increases, wavelength decreases
ν α 1/ λ or ν λ = c; where c is speed of light

## Slide 15: Communication entities: Data, Signals, Transmission and Channel
Data is the entity that is to be exchanged between different computers(voice, number, image..)
Signals electrical or electromagnetic representation of data
Data transmission is communication of data by the transmission or propagation of electromagnetic signals through either wired/wireless media (channel)

## Slide 16: Frequency
f = 3; t = 1/3 sec.
f = 1 ; t = 1 sec
f = 2 ; t = 1/2 sec
f = 0.5 ; t = 2sec
Spectrum: Range of frequencies comprising a signal
Bandwidth: Width of Spectrum

## Slide 17: Frequency perspective or Time perspective for communication
Radio channels, satellite TV channels, mobile communication signals, Wireless LAN signals all coexist together in the free space medium without interference!!.
HOW???
They Operate on different range of frequencies

## Slide 18: Electro magnetic spectrum
The electromagnetic spectrum is the range of all possible frequencies of electromagnetic radiation

## Slide 20: Bands suitable for communication
Radio Waves
Micro waves
Infra red waves
Visible spectrum

## Slide 21: Radio Waves

## Slide 22: Micro Waves

## Slide 23: Infra red waves

## Slide 24: Visible

## Slide 25: Frequencies for common wireless transmission

## Slide 27: Analog vs Digital signal

## Slide 28: Analog vs. Digital Signal